## Slide 1: AUTONOMOUS VEHICLE PROTOTYPE SYSTEM
For ECEN 5763 – Embedded Machine Vision and Intelligent Automation
By Siddhant Jajoo and Sarthak Jain
Under the guidance of Prof. Sam Siewert, University of Colorado Boulde
Platform Used – Jetson Nano

## Slide 2: Functional Capabilities
Accurate Detection of objects and targets using OpenCV transforms, Haar cascades and Histogram of Gradients.
Lane detection eliminating multiple lanes using history.
Pedestrian detection using HoG and non-maximum suppression.
Traffic signal and vehicle detection using Haar cascade
Set of services with scheduler, conforming with real-time requirements, to allow for a robust program design.
Processor and memory resources utilized to not exceed hardware capabilities but kept within optimal limits.

## Slide 3: Frame count per second
How high a frame rate did we achieve?
Initial moderate FPS
Final optimal FPS

## Slide 4: Frame count per second
How high a frame rate did we achieve?
Frames per second requirements for all threads | Minimum (fps) | Target (fps) | Achieved (fps)
Main thread | 10 | 15 | 27
Pedestrian detection service | 2 | 5 | 9
Lane following service | 6 | 10 | 13
Vehicle detection service | 6 | 10 | 12
Traffic sign service | 2 | 4 | 6
Service Si | Requested Frequency (1/Ti) (in Hz) | Deadline Frequency (1/Di) (in Hz) | WC frequency (1/Ci) (in Hz)
Main thread | 30 | 30 | 30
Pedestrian detection service | 10 | 10 | 10
Lane following service | 15 | 15 | 15
Vehicle detection service | 15 | 15 | 15
Traffic sign service | 7.5 | 7.5 | 8
DCT Analysis

## Slide 5: Processor Utilization
How much processor utilization is best?
Moderate CPU usage of 70%
Very high CPU usage of 96%

## Slide 6: Scheduler Specifications
Use of 5 semaphores
a. Causing deadlocks due to CFS
FIFO policy set
Services dedicated to cores
a. FPS achieved: 12-15
Scheduler implemented using DCT
Dynamic affinities to allow higher CPU usage
Problem in Linux scheduling (main thread hogging CPU-1)
Thread affinities set for main and other services.
Mutex implementation

## Slide 7: Lane Detection
Reduce the resolution by half and get the bottom half.
Create a mask to detect lanes in hsv and hls colour space.
Create ROI mask.
Bitwise and orginal image mask in step 2.
Apply canny threshold to detect lanes.
HoughlinesP to get lane coordinates.
Detect left and right lanes using slopes, averaging coordinates.
Using history to have smooth transitions using average intercept values and average slope values.

## Slide 8: Performance Analysis
  Factors contributing to high FPS –
    Scheduling policy
    Minimization of delays in main thread
    Individual services’ FPS
  Factors contributing to latency
    cvWaitKey
    Mutex locks

## Slide 9: Accuracy Analysis
PR plot of TP/(TP + FP) vs. TP/(TP + FN) for vehicle detection
Chart: Precision Recall curve for 10 points extrapolated from dataset of 100 subsequent frames
| 0.1 | 0.2 | 0.28000000000000003 | 0.4 | 0.5 | 0.6 | 0.67 | 0.8 | 0.8 | 1
Precision = TP/(TP + FP) | 0.5 | 0.33 | 0.67 | 0.8 | 1 | 0.75 | 0.67 | 1 | 0.57 | 1

## Slide 10: Accuracy Analysis
Histogram of data for vehicle detection
Chart: Histogram for data over dataset of 100 subsequent frames
| TP | FP | TN | FN
 | 74 | 48 | 174 | 30

## Slide 11: Accuracy Analysis
PR plot of TP/(TP + FP) vs. TP/(TP + FN) for pedestrian detection
Chart: Precision-Recall curve for 10 points extrapolated from dataset of 100 points
| 0.25 | 0.27 | 0.28000000000000003 | 0.33 | 0.38 | 0.4 | 0.44 | 0.47 | 0.5
Precision = TP/(TP + FP) | 0.7 | 0.75 | 1 | 0.67 | 0.75 | 1 | 0.67 | 0.78 | 0.85

## Slide 12: Accuracy Analysis
Histogram of data for pedestrian detection
Chart: Histogram for data over dataset of 100 images
| TP | FP | TN | FN
 | 127 | 28 | 188 | 70

## Slide 13: Output cases
Vehicle detection & Lane following

## Slide 14
Traffic sign recognition & Pedestrian detection

## Slide 15: Conclusion and Future scope
  Minimum requirements (achieved):
  Detection of each target without misses.
  Optimal requirements (achieved)
  All above minimum target requirements in multithreaded architecture to make prototype real-time with better FPS.
  Notifications to accelerate/decelerate
  Targets (future scope)
  Integration with Google map APIs for better navigation.
  Steering feedback to implement a lane departure warning system.